## Slide 1: Maximum Distance Gradient for Robust Image Registration
Chrouk Kasem

## Slide 2: Outline
Background: Image registration in medical imaging.
Motivation:
  Why mutual information in image registration?
  Limitations of MI and proposed improvements.
Proposed Robust Image Registration Method:
  What is MDG feature field and signed MDG feature field?
  Similarity measure.
  MDG feature space.
Implementation
Results and Discussion:
  Probing plots in rotation and translational axes.
  Registration of images.
Summary and Questions.

## Slide 3: Image Registration in Medical Imaging
CT
MR-T1
Image Registration
Blind Alignment
J. West et al. “Comparison and evaluation of retrospective intermodality image registration techniques.” Proceedings of the SPIE Conference on Medical Imaging, 1996.
Notes: Image registration is the problem of aligning a moving images to a fixed image spatially.
Each modality uses differenet sensing technology, therefore depicts different information about underlying anatomical structure and function,

## Slide 4: Why Mutual Information?
Doesn’t Assumes ANY LIMITING FUNCTIONAL RELATIONSHIP between image intensity pairs in the images
Measures statistical dependence between two image intensities
Philippe Cattin ”Intensity-based Registration“ MIAC, University of Basel, 2016

## Slide 5: Limitations Of MI And Proposed Improvements
Mutual information and image gradient
Local spatial information by image gradient:
Regional mutual information
Takes into account neighborhood regions of pixel pairs.
Russakoff et al. "Image similarity using mutual information of regions." In European Conference on Computer Vision. Springer, Berlin, Heidelberg, 2004.
Mutual information on extracted spatial
Features
Apply entropic measures on highly-dimensional features
Notes: Mutual information is a global metric, sensitive to occlusions, non-homogenious image intensity response. Maybe a result of overlap invariance, images of low resolution or interpolation methods
No spatial context

## Slide 6: Image Gradient
Equation of image gradient:
Gan et al. "Maximum distance-gradient for robust image registration." Medical image analysis 12.4 (2008).
Notes: Local edge information and globally defined spatial information.
Image gradient can be used to detect object boundaries, sudden intensity changes between voxels indicate a boundary. Only locally defined. Object boundaries occupy a small proportion of medical images, while anatomical structures and other locations in the background occupy a large proportion of voxels. This limits the effectiveness in image gradient feature in registration of medical images,=

## Slide 7: What is MDG Feature Field? Signed MDG Feature Field
Spatial Feature field called Maximum Distance Gradient (MDG) includes:
  Intensity Difference
  Distance
  The direction of voxel to a MDG SOURCE POINT
Encodes both local edge information and spatial information at a global level.
Gan et al. "Maximum distance-gradient for robust image registration." Medical image analysis 12.4 (2008).

## Slide 8: What is MDG Feature Field?
Intensity distance gradient between v1 and v2 is given by:
With
For each voxel, there exits an MDG source point, such that MDG vector field is :
where
Notes: We begin by defining the distance-gradient operator, this measure average rate at which intensity function I(v) changes between two voxels,
Magnitude of MDG gives the maximum average rate at which the intensity changes between v and any other voxels in the image.
It’s orientation is in the direction of the intensity between v and v bar

## Slide 9: Signed-MDG Feature Field:
Magnitude of the signed MDG feature field is:
Z feature space is defined as both intensity space, and MDG feature space:
Mutual information of two images in Z feature space is given by:
Orientation information of the MDG feature field can be expressed as:

## Slide 10: Similarity Measure
The proposed similarity metric is:
We are trying to find transformation parameters that maximise S(T):

## Slide 11: Implementation: Signed-MDG Field
Notes: In this implementation data sets from the RIRE project were used. This is my implementation of the MDG feature field on a MR-T1 weighted image in 3-D using the

## Slide 12: Implementation: Signed-MDG Field
Magnitude of signed-MDG feature field
MDG source points
Notes: Approximates conventional image gradient at object boundaries
In homogenous regions, it provides information of intensity, distance and voxel to MDG source point.

## Slide 13: Implementation - Multi-resolution Gaussian Pyramid
Level 0
Level 1
Level 2
Level 3
Notes: Find transformation at multiple resolutions formed by gaussian pyramid, which uses a gaussian blurr and scaled down images. This allows better performance for algorithm, wehere we can fine-tune the solution in the highest resolution.

## Slide 14: Implementation – At Each Level
2.1
Find MDG feature field
2.2
Find 4-dimensional mutual information:
Find 4-dimensional mutual information: 〖𝑀𝐼〗_𝑇 {𝓏_𝑓,𝓏_𝑟 }
2.3
Find orientation information of the signed MDG feature field:
Find orientation information of the signed MDG feature field: 𝐷(𝑇)
2.4
Compute similarity metric:
Compute similarity metric: 𝑆(𝑇)
2.1
Find MDG feature field
2.2
2.3
2.4
(1) For each rigid transformation range:
(3) Find parameters:
Notes: Rigid transformations where the rotational transformation uses trilinear interpolation. Done on boe overlapping and non-overlapping regions.

## Slide 15: Robustness of Registration of Images
Successful registration for 3-axes of translation by proposed similarity measure!
Translated image by -40 voxels in x-axis and 90 voxels in y-axis

## Slide 16: Registration of Images
Success Rate 95%
Cases of registration with perturbations in all axes and on rotational axes FAILED with MI4d*cos similarity metric
MR-T1 perturbed in all axes

## Slide 17: Probing Curves in Translational Axes
Notes: At resolution level 2: 64 x 64 x 13- using pre-aligned RIRE MR-T1 and CT images patient 001. The shape of the curve is significantly improved . Capture ranges of in-plane translational axis can be significantly improved

## Slide 18: Probing Curves in Rotational Axes
Notes: Decreases constantly, also indicating a longer capture range

## Slide 19: Summary
Maximum-distance gradient shows both local edge information and spatial information at a global level.
Longer capturing range than conventional 2-d mutual information measure.
Robust in detection of image translations.
Failed to align images with perturbations in all axes, and rotational axes.
Very slow performance compared to that of conventional 2-d MI and conventional image gradient with mutual information.

## Slide 20: Thank you!
Questions?